## Slide 1: Network Fundamentals
Presenter: Date:
Notes: This chapter introduces the OSI Layers notion.
It is also intended as a catch all chapter for all the basic stuff that people should know but might not know.
Depending on your audience you may chose to skip this chapter.

## Slide 2: Copyright
Copyright © by Forum of Incident Response and Security Teams, Inc.
FIRST.Org is name under which Forum of Incident Response and Security Teams, Inc. conducts business.
This training material is licensed under Creative Commons Attribution-Non-Commercial-Share-Alike 4.0 (CC BY-NC-SA 4.0)
FIRST.Org makes no representation, express or implied, with regard to the accuracy of the information contained in this material and cannot accept any legal responsibility or liability for any errors or omissions that may be made.
All trademarks are property of their respective owners.
Permissions beyond the scope of this license may be available at first-licensing@first.org
Notes: FIRST Training materials are available for non-commercial use under a CC license. We would appreciate if you let us know that you use it: Send a mail to first-sec@firtst.org with your feedback

## Slide 3: Network Fundamentals

## Slide 4: Overview
ISO – OSI Layers

## Slide 5: Network Layers
International Standards Organization (ISO)
Open Systems Interconnect (OSI) Layers

## Slide 6: Physical and Data-link Layers (layers 1 and 2)
Aka Network Access Layer (in the Internet Model)
Physical
  Media changes that carry information: voltage, phase
  Line coding: Manchester, NRZ, NRZ-I
  Data unit: bit
Data-link
  Data unit: frame (organizes bits in a frame)
  Provides physical addressing on a local network segment
  Separate in two:
    Media Access Control Layer (MAC): 802.3, 802.4, 802.5, 802.11abe
    Logical-link Control: 802.2

## Slide 7: Network Layer (layer 3)
Aka Internet Layer
Provides transport of data units between two points in the network
Provides logical (and global) addressing of machines in the network
Does not guarantee delivery
Allows for fragmentation
Data unit: Packet
Examples: Internet Protocol (IP)

## Slide 8: Transport Layer (layer 4)
Aka Transport (both models agree!) 
Provides logical connection between applications
Provides addressing of applications on a single system (via port numbers)
Data unit: segment
In some modalities like TCP provides virtual circuit and ensures data ordering and no loss of packets
Typical for TCP is the 3-way handshake
Examples: TCP, UDP

## Slide 9: Session Layer (layer 5)
Part of the Internet model Application layer
Managing sessions between application (think state, like authentication)
Examples: HTTP, SMTP, NetBIOS
Addressing: some protocols provide logical endpoint

## Slide 10: Presentation Layer (layer 6)
Part of the Internet model Application layer
Provides uniform data representation across multiple architectures and platforms
Examples: images, file encryption

## Slide 11: Application Layer (layer 7)
This is where the application lives
Part of the Internet model Application layer
Notes: Put special stress on the overloading of the name.