## Slide 1: IPv6 Security Lab Setup
Author: Frank Herberg <frank.herberg@switch.ch>

## Slide 2: Copyright
Copyright © by Forum of Incident Response and Security Teams, Inc.
FIRST.Org is name under which Forum of Incident Response and Security Teams, Inc. conducts business.
This training material is licensed under Creative Commons Attribution-Non-Commercial-Share-Alike 4.0 (CC BY-NC-SA 4.0)
FIRST.Org makes no representation, express or implied, with regard to the accuracy of the information contained in this material and cannot accept any legal responsibility or liability for any errors or omissions that may be made.
All trademarks are property of their respective owners.
Permissions beyond the scope of this license may be available at first-licensing@first.org
Notes: FIRST Training materials are available for non-commercial use under a CC license. We would appreciate if you let us know that you use it: Send a mail to first-sec@firtst.org with your feedback

## Slide 3: virtual machine setup
Attacker
Victim 1
Victim 2
Router
2 Switches
Webserver

## Slide 4: Example Setup with 5 VMs
R1
SW1
SW2
Attacker
Using THC IPv6 attack toolkit
08:00:27:AA:AA:AA
fe80:a00:27ff:feaa:aaaa
2001:db8:1::a00:27ff:feaa:aaaa
GW: fe80::a00:27ff:fe11:1111
08:00:27:BB:BB:BB
fe80:a00:27ff:febb:bbbb
2001:db8:1::a00:27ff:febb:bbbb
GW: fe80::a00:27ff:fe11:1111
Randomize Identifiers disabled
08:00:27:66:66:66
fe80:a00:27ff:fe66:6666
2001:db8:1::a00:27ff:fe66:6666
GW: fe80::a00:27ff:fe11:1111
Privacy Extensions disabled
2001:db8:2::2
GW: 2001:db8:2::1
eth0: forwarding enabled
2001:db8:1::1
fe80::a00:27ff:fe11:1111
radvd:
Prefix 2001:db8:1::/64
eth1:
2001:db8:2::1
Win7
﻿Webserver: http://[2001:db8:2::2]/
Notes: EUI-64 insert FFEE to get 64 Bits (from 48 Bit MAC)
Modified EUI-64: toggle Bit 7 (08=>0A)
0000 i000  8
0000 i0i0 =>10=>A
Show 3 clients live

## Slide 5: Virtual Machines
Attacker
  Linux (Ubuntu)
  Wireshark
  THC IPv6 Attack Tools https://github.com/vanhauser-thc/thc-ipv6
  MAC address defined in VM (666666)
  Privacy extensions disabled
Victim 1
  Windows
  Randomize identifiers disabled
Victim 2
  Linux (Ubuntu)
  If Network Manager installed => creates static route contrary to specification => flush routes

## Slide 6: Virtual Machines
Router
  Linux, 2 interfaces defined in Virtual Box  2 virtual Switches
  Static IP configuration of both interfaces
    /etc/network/interfaces
  Routing enabled
    /etc/sysctl.conf
  radvd installed und configured
    /etc/radvd.conf
Webserver
  Apache
  Static IP configuration