## Slide 1: IPv6 Security Training Part 2
Presenter
Author: Frank Herberg frank.herberg@switch.ch
Version: 06/2019 b
Notes: Startfolie fixes Bild Bsp. 1

## Slide 2: Copyright
Copyright © by Forum of Incident Response and Security Teams, Inc.
FIRST.Org is name under which Forum of Incident Response and Security Teams, Inc. conducts business.
This training material is licensed under Creative Commons Attribution-Non-Commercial-Share-Alike 4.0 (CC BY-NC-SA 4.0)
FIRST.Org makes no representation, express or implied, with regard to the accuracy of the information contained in this material and cannot accept any legal responsibility or liability for any errors or omissions that may be made.
All trademarks are property of their respective owners.
Permissions beyond the scope of this license may be available at first-licensing@first.org
Notes: FIRST Training materials are available for non-commercial use under a CC license. We would appreciate if you let us know that you use it: Send a mail to first-sec@firtst.org with your feedback

## Slide 3: Agenda
Short Introduction to IPv6
Introduction to IPv6 Security
Local Protocol Attacks & Mitigation
Securing Transition Mechanisms
 Perimeter Security & Firewalls
NAT & Security
Reconnaissance with IPv6

## Slide 4: Important
In the Training Lab
Only execute attack tools as instructed!
In your productive environment
Don't try the attack tools!
Notes: request

## Slide 5: Perimeter Security

## Slide 6: What you will learn
Basic Firewalls Issues with IPv6…
…and how to tackle them
Recommendations for IPv6 Firewall policies
Extension Header Threats
Fragmentation Issues
Multicast and Security

## Slide 7: Typical Perimeter Examples: DMZ, Internal Network
www SMTP
ISP
Internet
Internal
Network
VLANs with managed clients
Internal Server Zone
DMZ

## Slide 8: IPv6 & Firewalls

## Slide 9: Basic IPv6 Firewall Issues
IPv6 is highly complex for Firewalls (e.g. EH)
There is nothing like an IPv6 standard
  only a bunch of RFCs – partially conflicting
IPv6 design is still a moving target
  e.g. RFC 6564: April 2012 (Uniform Format for EHs)
Low maturity of Implementation
  unstable Software and frequent Updates
Complexity hinders (ASIC-)Performance
  feature parity doesn't mean you can use appliance under full productive load
Notes: repetition!

## Slide 10: IPv4 & IPv6 Firewall Policies
Different Dual Stack configuration approaches around:
Firewall-Policy #95 from to service action
IPv6
IPv4
Firewall-Policy #96 for IPv6
from to service action
Firewall-Policy #95 for IPv4
from to service action
Firewall B for IPv6 Policy #95
from to service action
Firewall A for IPv4 Policy #95
from to service action
Add new Protocol to existing policy*
What you might prefer…
B) Maintain different Policies for v4 and v6**
…what you might get…
C) Leave existing v4 FW and add a second for v6 …and what you should consider!
**Fortinet, **Cisco,*Palo Alto
Notes: see next slide

## Slide 11: Separate IPv6 FW might be advantageous
no upgrade to existing stable IPv4-FW needed
installing updates for IPv6-FW (which are likely) easier to maintain
easier to change IPv6-FW if needed
maybe migrate IPv4-Policies to new FW later on and switch old one off
Notes: likely to have frequent updates / patches for IPv6 FW
no downtimes for productive ipv4 fw

## Slide 12: How to tackle IPv6 Firewall Issues?
Wait until everything is settled
Know which features you need - learn IPv6 ;-)
Talk to your vendor(s) - What's their IPv6 roadmap?
Evaluate and Test!
Test performance also (or have other evidence)
Notes: repetition!

## Slide 13: IPv6 Firewall Policies

## Slide 14: Recommendations for IPv6 Firewall policies
v6 FW policies should match v4 policies in most cases
  "from to service action" is the same for both protocols
Allow only allocated addresses
  Unlike v4 in v6 only a fraction of the address space is allocated
  List of legitimate v6 addresses is maintainable
  see IANA IPv6 Global Unicast Address Assignments:
   http://www.iana.org/assignments/ipv6-unicast-address-assignments/ipv6-unicast-address-assignments.xml (see next page)
Do Antispoofing Filtering (as in v4)
  Ingress filter for source addresses from internal address space
  Egress filter for source addresses other than internal address space
Notes: 1.: (address groups/zones might be different between 4 and 6 depending on addressing plan) ex: allow port 80 from internal-zone to internet
2.: ingress source / egress destination, currently about 50 entriesin the IANA list
3.: those pakets are not legitimate (but spoofed)

## Slide 15
for your reference
Notes: currently about 50 entries

## Slide 16: Recommendations for IPv6 Firewall policies
IPv6 addresses that should be denied (both directions)
  Unspecified address ::, loopback address ::1
  IPv4-mapped IPv6 addresses
  ::ffff:0.0.0.0/96, ::224.0.0.0/100, ::127.0.0.0/104, ::0.0.0.0/104, ::255.0.0.0/104
  False 6to4 addresses (192.168.0.0/16, 10.0.0.0/8, loopback, etc)
  2002:e000::/20, 2002:7f00::/24, 2002:0000::/24, 2002:ff00::/24, 2002:0a00::/24, 2002:ac10::/28, 2002:c0a8::/32,
  Link-local addresses fe80::/10
  Reserved for documentation addresses 2001:db8::/32
  Unique Local Addresses (ULA RFC 4193) fc00:: /7
  All Multicast ff00:: /8 or Site Scope Multicast ff05::/16
Notes: should not travers the perimeter /or/ should not appear on the network at all
::ffff:0.0.0.0/96 IPv6 representation of v4 addresses in software ("wrong protocol")
::224.0.0.0/100 IPv4 multicast
False 6to4 example: 2002:0a00::/24: means IPv4 private address space 10.0.0.0/8
Multicast: Source address

## Slide 17: Recommendations for IPv6 Firewall policies
More…
Deprecated addresses
  3ffe::/16 Former 6bone, now decommissioned
  fec0:: /10 Site-local Unicast – deprecated by RFC 3879 (replaced by ULA)
  ::/96 IPv4-compatible IPv6 address – deprecated by RFC4291
  0200:: /7 OSI NSAP-mapped prefix set (RFC4548) – deprecated by RFC4048
Notes: More IPv6 addresses that should be denied (both directions)
These addresses are deprecated and should not appear on the public Internet.
::/96 means 96 bits zero (and remaining 32 bits for ip4 addr) RFC 4291

## Slide 18: Recommendations for IPv6 Firewall policies
Additional filtering of unallocated address space ("Bogons" = faked addresses)
You can block IP space that has been allocated to a RIR, but not yet assigned by that RIR to an actual ISP or other end-user
These addresses are commonly found as the source addresses of DDoS attacks
Team Cymru maintains a list (currently >63000 entries /31../64) :
http://www.team-cymru.org/Services/Bogons/fullbogons-ipv6.txt
This list has significant changes every day – so only use it if you can keep your filters current!
For more information, see:
http://www.team-cymru.org/Services/Bogons/
Notes: fine-grained filter of not assigned address space
one idea: prepare this filter just in case you face a DDOS attack

## Slide 19: Recommendations for IPv6 Firewall policies
Filter unused transition mechanisms
Block Inbound destination 2001:0000:://32 (Teredo)
Block Inbound destination 2002::/16 (6to4)
Block outbound IPv4 UDP Port 3544 (Teredo)
Block outbound IPv4 Protocol 41 (6to4, 6rd, ISATAP)
Please refer to Section "Transition Mechanisms" for details
Notes: recommendations can be found on the internet
or in the book "ipv6 security"
"only apply what you've understood"  take your time

## Slide 20: Recommendations for filtering ICMPv6 (RFC 4890)

## Slide 21: ICMPv6
Internet Control Message Protocol for IPv6, RFC 4443
ICMPv6 is defined as Extension Header No. 58
ICMPv6 Types & Codes:
http://www.iana.org/assignments/icmpv6-parameters
for your reference
Notes: repetition

## Slide 22: ICMPv6 Types
Error-Messages (1-127)
1:Destin. Unreach. 2:Packet too big (PMTUD) 3:Time Exceeded (Hop Limit) 4:Parameter Problem
Info-Messages (Ping)
128:Echo Request 129:Echo Reply
Multicast Listener Discovery (MLD, MLD2)
130:Multicast Listener Query 131/143:Multicast Listener Report/2 132:Multicast Listener Done
Neighbor Discovery (NDP), Stateless Autoconfiguration (SLAAC)
133:Router Solicit. 134:Router Advert. 135:Neighbor Solicit (DAD) 136:Neighbor Advert. (DAD) 137:Redirect Message
Other (Router Renumbering, Mobile IPv6, Inverse NS/NA,…)
138-153 (not 143)
138: Router Renumbering 139/140:ICMP Node Info 141/142: Inverse Neighbor Discovery
144-147: Mobile IPv6 Home Agent Address Discovery Request/Reply & Mobile Prefix Solicit. / Advert.
148/149: SEND Cert. Path Solicit/Advert.
150: Experimental Mobility Protocols
151-153: Multicast Router Discovery (Advert./Solicit./Termination)
Notes: repetition

## Slide 23: Recommendations for Filtering ICMPv6
Aim of RFC 4890:
  Allow propagation of ICMPv6 messages needed to maintain functionality of the network
  but
  Drop messages posing potential security risks
Notes:   NEEDED "Packet too Big" for Path MTU Discovery
  RISK: Network Discovery Protocol (like Router Advertisements)

## Slide 24: ICMPv6 Security Concerns (according to RFC 4890)
Denial-of-Service Attacks
Probing to identify topology and hosts
Redirection Attacks using the Redirect message
Renumbering Attacks (Renumbering messages are required to be authenticated with IPsec)
Covert conversation through the payload of ICMPv6 error messages

## Slide 25: Ongoing discussion between the experts
Excerpt from ipv6hackers mailing list on "Operational ICMPv6 Filtering":
  > I can only strongly recommend people to not invent something new on their own, but read this RFC (4890) first...
  (Gert D., RIPE-NCC chair)
  >> ...which is way to open. written from a networker perspective, not a security perspective. Greets, Marc
  (Marc H., thc-ipv6)
Notes: Gert Döring
Marc Heuse author of thc-tools
ipv6hackers mailing list is RECOMMENDED reading

## Slide 26: More Filtering ICMPv6 discussion
There is also a new draft (March 2012):
  "Recommendations for filtering ICMP messages"
  http://tools.ietf.org/html/draft-ietf-opsec-icmp-filtering-03
  But this is work in progress!
  RFC 4890 ist still a good source
Notes: DRAFT is already expired: September 13, 2012

## Slide 27: Some ICMPv6 Filtering Considerations
Options:
Block/Allow ICMPv6 traffic based on type and code
Stateful Filtering can limit even allowed types to those that could legitimately be part of permitted traffic flows
Deep Packet Inspection can examine header and data part of a ICMPv6 packet for non-compliance or covert channel
Notes: Example for stateful: Echo Reply only if Echo Request
DPI: Safer but also more intrusive
how to judge this: also a matter of personal philosophy

## Slide 28: Filtering ICMPv6 - protocol internal measures
Exercise: Think about protocol internal measures that prevent the distribution of only locally needed ICMPv6 messages across network boundaries.
(See the protocol dump on the next slide.)
Notes: for advanced students! 

## Slide 29: ICMPv6 Type 134 Code 0
…
protocol internal measures that prevent the distribution of only locally needed ICMPv6 messages across network boundaries?

## Slide 30: Filtering ICMPv6 - protocol internal measures
ICMPv6 messages sourced by link-local addresses are not forwarded across Layer-3 devices
IPv6 nodes discard certain ICMPv6 packets with hop limit <255
Notes: receiver drops packet if it has traversed a hop

## Slide 31: ICMPv6 Traffic that will be dropped anyway
Number | Type | Hop Limit = 255 | Use LL addresses
1-4 | Error Messages |  | 
128,129 | Echo Request / Reply |  | 
130-132,143 | Multicast Listener Discovery |  | X
133-136 | RS/RA NS/NA | X | 
137 | Redirect | X | 
138 | Router Renumbering |  | 
139,140 | ICMP Node Info Query / Resps. |  | 
141,142 | Inverse Neighbor Discovery | X | 
144,145 | Home Agent Address Discovery |  | 
146,147 | Mobile Prefix S/A |  | 
148,149 | Certification Path S/A | X | 
150 | experimental mobility protocols |  | 
151-153 | Multicast Router S/A/Termination |  | X

## Slide 32: ICMPv6 Traffic that will be dropped anyway
Error-Messages (1-127)
1:Destin. Unreach. 2:Packet too big (PMTUD) 3:Time Exceeded (Hop Limit) 4:Parameter Problem
Info-Messages (Ping)
128:Echo Request 129:Echo Reply
Multicast Listener Discovery (MLD, MLD2)
130:Multicast Listener Query 131/143:Multicast Listener Report/2 132:Multicast Listener Done
Neighbor Discovery (NDP), Stateless Autoconfiguration (SLAAC)
133:Router Solicit. 134:Router Advert. 135:Neighbor Solicit (DAD) 136:Neighbor Advert. (DAD) 137:Redirect Message
Other (Router Renumbering, Mobile IPv6, Inverse NS/NA,…)
138-153 (not 143)
138: Router Renumbering 139/140:ICMP Node Info 141/142: Inverse Neighbor Discovery
144-147: Mobile IPv6 Home Agent Address Discovery Request/Reply & Mobile Prefix Solicit. / Advert.
148/149: SEND Cert. Path Solicit/Advert.
150: Experimental Mobility Protocols
151-153: Multicast Router Discovery (Advert./Solicit./Termination)

## Slide 33: ICMPv6 types that need further attention:
Error-Messages (1-127)
1:Destin. Unreach. 2:Packet too big (PMTUD) 3:Time Exceeded (Hop Limit) 4:Parameter Problem
Info-Messages (Ping)
128:Echo Request 129:Echo Reply
Other (Router Renumbering, Mobile IPv6, Inverse NS/NA,…)
138-153 (not 143)
138: Router Renumbering 139/140:ICMP Node Info 144-147: Mobile IPv6 Home Agent Address Discovery Request/Reply & Mobile Prefix Solicit. / Advert.
150: Experimental Mobility Protocols

## Slide 34: Error messages 1/2
Error messages that are essential to the establishment and maintenance of communications
  Destination Unreachable (Type 1)
  Packet Too Big (Type 2) PMTUD
  Time Exceeded (Type 3) - Code 0 (hop limit exceeded in transit)
  Parameter Problem (Type 4) - Codes 1 (unrecognized Next Header type encountered) and 2 (unrecognized IPv6 option encountered)
 "must not be dropped"
Notes: essential for communication

## Slide 35: Error messages 2/2
Other Error messages (not essential for communication)
  Time Exceeded (Type 3) – Code 1 (fragment reassembly time exceeded)
  Parameter Problem (Type 4) – Code 0 (erroneous header field encountered)
 "normally should not be dropped"

## Slide 36: Connectivity checking messages
Connectivity checking messages
  Echo Request (Type 128)
  Echo Response (Type 129)
"must not be dropped" according to the RFC
hence a risk of scanning attacks
RFC 4890: "For Teredo tunneling to nodes on the site to be possible, it is essential that the connectivity checking messages are allowed through the firewall."
 might be another argument to drop them
Notes: ping: This is according to the RFC, and there is a section normally should not be dropped

## Slide 37: Mobile IPv6 Messages
Mobile IPv6 messages that are needed to assist mobility:
  Home Agent Address Discovery Request (Type 144)
  Home Agent Address Discovery Reply (Type 145)
  Mobile Prefix Solicitation (Type 146)
  Mobile Prefix Advertisement (Type 147)
"normally should not be dropped"
 but only needed if a Mobile IPv6 Home Agent is used

## Slide 38: ICMPv6 types that need further attention:
Other
138-153 (not 143)
138: Router Renumbering
139/140:ICMP Node Info Discovery Request/Reply & Mobile Prefix Solicit. / Advert.
150: Experimental Mobility Protocols
Undefined Error-Messages
Undefined Info-Messages

## Slide 39: Undefined or Experimental ICMPv6 Types
Undefined Types:
  Undefined Error Message Types 5-99, 102-126
  Undefined Informational Messages 154-199, 202-254
"A Policy should be defined."
(If you choose to drop currently undefined ICMPv6 types, remember to review the set of messages affected in case new message types are assigned by IANA http://www.iana.org/assignments/icmpv6-parameters)
Experimental Types:
  Type 150 ("Seamless Mobility") is Experimental
  Experimental Error Messages Types 100-101
  Experimental Inform. Messaged 200-201
"Should be dropped unless a good case can be made."

## Slide 40: What's still left?
Other (Router Renumbering, Mobile IPv6, Inverse NS/NA,…)
138: Router Renumbering
139/140:ICMP Node Info Discovery Request/Reply & Mobile Prefix Solicit. / Advert.

## Slide 41: ICMPv6 Filtering Overview (Transit)
Number | Type | Action | Remark
1-4 | Error Messages | allow | are needed
128,129 | Echo Request / Reply | allow (or deny) | you decide
130-132,143 | Multicast Listener Discovery |  | ignore
133-136 | RS/RA NS/NA |  | ignore
137 | Redirect |  | ignore
138 | Router Renumbering | deny | 
139,140 | ICMP Node Info Query / Resps. | deny | 
141,142 | Inverse Neighbor Discovery |  | ignore
144,145 | Home Agent Address Discovery | deny | unless Mobile IPv6 is used
146,147 | Mobile Prefix S/A | deny | unless Mobile IPv6 is used
148,149 | Certification Path S/A |  | ignore
150 | experimental mobility protocols | deny | 
151-153 | Multicast Router S/A/Termination |  | ignore
Other | undefined or experimental | deny | unless needed
Notes: ignore => will be dropped anyway (Link Local or Hop limit)
Error Messages are:
1 Destination unreachable /Code 0-6
2 Packet too big (required for Path MTU Discovery)
3 Time exceeded (Hop Limit / Fragment reassembly)
4 Parameter Problem (e.g. unrecognized Next Header)

## Slide 42: ICMPv6 Filtering Overview (to interface)
Number | Type | Action | Remark
1-4 | Error Messages | allow | are needed
128,129 | Echo Request / Reply | allow (or deny) | you decide
130-132,143 | Multicast Listener Discovery | allow** | 
133-136 | RS/RA NS/NA | allow** | 
137 | Redirect | deny | unless needed, (see 4.4.4)
138 | Router Renumbering |  | ignore
139,140 | ICMP Node Info Query / Resps. | deny | unless needed
141,142 | Inverse Neighbor Discovery | allow | 
144,145 | Home Agent Address Discovery |  | ignore
146,147 | Mobile Prefix S/A |  | ignore
148,149 | Certification Path S/A | allow | 
150 | experimental mobility protocols |  | ignore
151-153 | Multicast Router S/A/Termination | allow | 
Other | undefined or experimental | deny | unless needed
Notes: MLD must be accepted to participate in Multicast Routing
133/134 RS/RA necessary for a variety of reasons, most notably IPv6 end-node autoconfiguration
135/136 NS/NA DAD and Layer 2 Address Resolution (MAC to IP)
for more details see RFC (Appendix A of RFC 4890)

## Slide 43: ICMPv6 Traffic to local FW interface
Section 4.4 of RFC 4890 recommends filtering rules for ICMPv6 traffic addressed to an interface on a firewall.
Remarks:
"For a small number of messages, the desired behavior may differ between interfaces on the private side of the firewall and the those on the public Internet side of the firewall."
"Host firewalls can be treated as end site firewalls but the special considerations discussed in Section 4.2 may be relevant because the firewall is not a router."
for your reference
Notes: more section 4.4

## Slide 44: ICMPv6 Filtering: RFC 4890 is comprehensive!
Detailed notes on individual ICMPv6 messages can be found in Appendix A
Example Script for Netfilter / ip6tables can be found in Appendix B

## Slide 45: DOS using ICMPv6 from outside
Notes: known DAD DOS only works local
can ICMPv6 also be DOSsed from outside?

## Slide 46: Remote Neighbor Cache Exhaustion Attack
Problem:
Aggressive IPv6 address scanning consums router resources
Big subnet, small neighbor cache table
neighbor cache is similar to IPv4 ARP entry (ip addr:phys. addr)
 A ping scan floods neighbor cache table (fast)
Notes: keep state until reachability information is complete

## Slide 47: Remote Neighbor Cache Exhaustion Attack
Impact:
Some routers break all interfaces
Some routers break targeted interface
At least legitimate entries are evicted from table
Notes: how severe this really is, you find different opinions, but you can test it for your devices

## Slide 48: Remote Neighbor Cache Exhaustion Attack
Mitigation:
Ingress ACL allowing only valid destination and dropping the rest
Maybe you have a built-in Rate limiter
Cisco Feature: "IPv6 Destination Guard"
  (is coming...)
Workaround: Allocate /64, configure /120 (brakes SLAAC, maybe more)
Notes: valid means actually used address range
for point-to-point-links /127

## Slide 49: Resource Consumption Attack
Problem (example):
Attacker sends large amount of packets to firewall with Hop Limit = 1
Firewall decremends to 0, drops the packet and
sends an ICMPv6 Time exceeded message for each packet
Mitigation:
Rate limit ICMPv6 error messages to avoid Resource Consumption Attacks:
ipv6 icmp error-interval <milliseconds>
Notes: keeps the FW busy

## Slide 50: Extension Headers & Security

## Slide 51: IPv6 Extension Headers
IPv6-Header
Next Header = 6 (TCP)
TCP-Header
IPv6-Header
Next Header = 43 (Routing)
Routing-Hdr.
Next Header = 44 (Fragment)
Frgmnt-Hdr.
Next Header = 6 (TCP)
IPv6-Header
Next Header = …
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
DATA
…
TCP-Header
DATA
…
TCP-Header
DATA
…
Notes: IPv6 Header has a fixed length of 40 bytes (simple fast processing)
For Options additional Header can be included / chained
If new Options are required new EH can be defined
EH are defined in RFC 2460, Section 4
Protocol numbers listed in http://www.iana.org/assignments/protocol-numbers/protocol-numbers.xml

## Slide 52: Extension Header Examples
No. | Name | Functions | Remarks
0 | Hop-by-Hop-Options | carries options for hops, e.g. Router Alert (for MLD, RSVP) | must be examined by every hop on the path Must be first EH, only one allowed per packet
60 | Destination Options | carries options for destination (e.g. for Mobile IPv6) | processed by destination node only*
43 | Routing Header | Lists IPv6 nodes that must be "hopped" on the way to dest. | 
44 | Fragmentation Header | Fragmentation (at source) | only source can fragment, processed by destination node only
Other examples: 6:TCP, 17:UDP, 58:ICMPv6, 50/51: ESP/AH (IPSec)
Notes: *Exception: A Destination Options Header in front of a Routing Header means Routers must process the header

## Slide 53: Inspecting packets with EH is challenging…
The number of EHs is not limited
The number of options within an (Hop-by-Hop or Destination) Options Header is not limited
There is no defined order of EHs (only a recommendation)
  (Exception: Hop-by-Hop Options Header must be first and nonrecurring)
EH have different formats
Notes: for a FW this is a complex thing to do
( max size of packet 64 kbit )

## Slide 54: According to RFC2460, Section 4 "IPv6 Specification"
"In-between-Boxes" (such as Firewalls) are not intended to examine EHs...
  "With one exception, extension headers are not examined or processed by any node along a packet's delivery path, until the packet reaches the node."
…but the destination node must completely process all EHs
  "any order and occurring any number of times in the same packet"
Notes: Security Issue 1: No network security device can protect end host
Security Issue 2: any order / any occuring number  invitation to test robustness of endhost, try DOS/crash (it has to process all the information)
the one exception: Hop-by-hop Options Header

## Slide 55: Remark: Processing of Extension Headers
Only to reach the Upper Layer Protocol information (e.g. TCP Port) Firewalls have to parse through all EH
which adds complexity and work load to the standard paket filter job
Notes: Firewalls only parse – no interpretation / inspection needed here

## Slide 56: A corrective (partly) …
RFC 6564, April 2012:
  "A Uniform Format for IPv6 Extension Headers"
This document proposes one step in easing the inspection of EHs by middleboxes
at least for new EHs
Notes: RFC 6564: Hdr Ext Length
Parsing EHs often done in Application-specific Integrated Circuits (ASICs) in order to maintain wirespeed
any new IPv6 extension header will break IPv6 deployments that use these existing capabilities
This document proposes one step in easing the inspection of extension headers by middleboxes

## Slide 57: Extension Header Threats
Exercise: Think about possible threats utilizing Extension Headers.

## Slide 58: Possible Threat: High Number of EHs
An attacker could create packet with high number of EH
 to try to avoid FW / IPS
might crash or DOS the destination system
Mitigation option: Drop packets with more than x EHs
IPv6-Header
Next Header = …
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
TCP-Header
DATA
…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…
Ext-Hdr.
Next Header =…

## Slide 59: Possible Threat: Manipulation of the EHs
An attacker could perform header manipulation to create attacks
  Fuzzing (try everything – it's not limited)
  add (many) unknown options to an EH, e.g. Hop-by-hop-Options
The Destination node / Server has to look into crafted EHs
Destination System might crash
Mitigation option: Perform sanity checks on EH (format / no. of options)
IPv6-Header
Next Header = 43 (Routing)
EH
Next Header = 0 (Hop-by-hop Options)
EH
)/&(/&"%ç&+=&+=/%ç/%/=()/
TCP-Header
DATA
…
Notes: IANA defined options: www.iana.org/assignments/ipv6-parameters/ipv6-parameters.xml

## Slide 60: Possible Threat: Covert Channel
An attacker could use Extension Headers as a covert channel
to exchange payload undiscovered
Mitigation option: Drop unknown EH
IPv6-Header
Next Header = 43 (Routing)
EH
Next Header = 0 (Hop-by-hop Options)
EH
information exchange
TCP-Header
DATA
…
Notes: this might not help because attack information is in the data fields of the EH

## Slide 61: Possible Threat: Router Alert Attack
Send a lot of packets with Router alert option
This forces all Router along the path to analyze packet deeply
and cause resource consumption (100% CPU)
Mitigation option:
Filter out non-allocated values for Router Alerts
http://www.iana.org/assignments/ipv6-routeralert-values/ipv6-routeralert-values.xml
IPv6-Header
Next Header = 0 (Hop-by-Hop)
EH
Router Alert!
TCP-Header
DATA
…
IPv6-Header
Next Header = 0 (Hop-by-Hop)
EH
Router Alert!
TCP-Header
DATA
…
IPv6-Header
Next Header = 0 (Hop-by-Hop)
EH
Router Alert!
TCP-Header
DATA
…
IPv6-Header
Next Header = 0 (Hop-by-Hop)
EH
Router Alert!
TCP-Header
DATA
…
IPv6-Header
Next Header = 0 (Hop-by-Hop)
EH
Router Alert!
TCP-Header
DATA
…
IPv6-Header
Next Header = 0 (Hop-by-Hop)
EH
Router Alert!
TCP-Header
DATA
…
Notes: Router Alert Option Values: 0=contains MLD message 1= contains RSVP message
IANA maintains a list of allocated Router Altert Values (currently 1-68) RSVP, MLD-message
Filter out all other values
69-65502 Unassigned
65503-65534 Reserved for experimental use

## Slide 62: Routing Header Type 0 Attack ("Source Routing")
1998 defined in RFC 2480
"The Routing header is used by an IPv6 source to list one or more intermediate nodes to be "visited" on the way to a packet's destination."
2007 CanSecWest-Conference Talk
 RH Type 0 can be used for dumb Firewall Bypass
 RH Type 0 can be used for Amplification Attacks (88-fold)
  attacker sends a packet with RH containing
  A -> B -> A -> B -> A -> B -> A -> B -> A ....
  Packet will loop multiple time on the link A-B and cause Link Saturation
Dec 2007 RFC 5095: "Deprecation of Type 0 Routing Headers in IPv6"
Notes: IPv6 History
Source Routing means the sender defines the route of the packet; can add multiple hops

## Slide 63: Routing Header Type 0 Attack
Mitigation: block Type 0 Routing Header Traffic
make sure "no ipv6 sourceroute" is set
Default IOS changed in 12.4(15)T: no need to type "no ipv6 sourceroute"
Link to CanSecWest 2007 Conference Slides:
  http://www.secdev.org/conf/IPv6_RH_security-csw07.pdf

## Slide 64: Examples for EH Filtering
IOS-Example: block unknown EH
ipv6 access-list BLOCKHEADER
deny ipv6 any any log undetermined-transport
ip6tables-Example: block Type 0 Routing Header Traffic
ip6tables -A INPUT -m rt--rt-type 0 -j DROP
ip6tables -A FORWARD -m rt--rt-type 0 -j DROP
ip6tables -A OUTPUT -m rt--rt-type 0 -j DROP
Notes:   IOS (starting with Release 12.2(13)T and 12.0(23)S)

## Slide 65: If you want to test EH Filter capabilities
There are tools to test your Security Devices:
Scapy6
  utility that can create custom IPv6 packets with crafted extension headers / also for fragmentation
ISIC6 (IP Stack Integrity Checker for v6)
  utility that generates random IPv6 packets (protocol fuzzer and flooder)
fuzz_ipv6 (part of the THC IPv6 toolsuite)
  different options to fuzz headers
also look at other THC tools (implementation6/6d)
for your reference

## Slide 66: Fragmentation Issues (still Extension Headers & Security)

## Slide 67: What is Fragmentation?
Splitting an IP packet into smaller packets (receiver has to reassemble it)
IPv6-Header
Transport-Header
Data
IPv6-Header
Transport-Header
Data
Fragmnt.Header
IPv6-Header
Data
Fragmnt.Header
Fragment 1
MTU
MTU
"Packet too big"
Oversized Packet
Fragment 2
Notes:       Fragmentation is only allowed by Sender (not any hop)  performance reasons
      Path MTU Discovery is used instead (RFC 1981)
1280 Bytes is defined as minimum MTU for IPv6
1500 Bytes is standard MTU for Ethernet / IPv6

## Slide 68: Fragmentation Issues 1/3
Attacker can try to bypass filtering/detection (IDS/IPS evasion technique)
  by putting the attack into many small fragments
  by combination of multiple extension headers and fragmentation so that layer 4 header is in 2nd fragment
  Analyzing becomes more difficult / resource consuming
Notes: THC-tool: fragmentation6

## Slide 69: Fragmentation Issues 2/3
Attacker can exploit weaknesses in the destination
  by crafting fragments if method of reassembling isn't solid (Example: Overlapping fragments, nested fragments)
Notes: THC-tool: fragmentation6

## Slide 70: Fragmentation Issues 3/3
Attacker can DOS destination
  send lots of incomplete fragment sets (M-flag 1  more fragments)
  End host has to wait for timeout, allocates kernel memory for reassembly
  typical reassembly timeout is 60s (ICMPv6 Type 3 Code 1)
Notes: THC-tool: fragmentation6

## Slide 71: Preventing Fragmentation Attacks
You can
monitor the amount of fragmented packets
high increase might indicate attack
block fragments which are below a certain size (if not the last one of a set [M-flag=0])
don't appear in proper communication
look for Inspection capabilities of fragmented packets
  e.g. Cisco: Virtual Fragment Inspection (VFR)
ipv6 virtual-reassemly
Notes: According to IPv6 RFCs reassembly inbetween is not intended
Hardware Ressources are needed for performance

## Slide 72: End of Extension Headers & Fragmentation

## Slide 73: Multicast & Security

## Slide 74: Multicast in a nutshell
No Broadcast exists in IPv6
Multicast is used for 1-to-many communication
Multicast is used for traditional multimedia applications
but also for Neighbor Discovery or DHCPv6
Multicast Addresses start with "FF"
  FF + 4bit flags + 4bit scope + 112 bits group identifier
  Typical Scopes: 2 = Network segment , 5 = Site, E = Global
  ff02::1 all local nodes, ff05::1:3 all DHCP servers on local site
defined in RFC 4291, 2.7
for your reference
Notes: repetition

## Slide 75: Multicast Rogue DHCPv6 communication
Attackers can communicate with DHCPv6 Servers via their Multicast addresses (ff02::1:2, ff05::1:3 )
Mitigation: Block this traffic at the network perimeter

## Slide 76: Multicast Amplification Attack
Attackers can send packets (with spoofed source address) to Multicast Addresses to amplify traffic volumes (DDoS)
RFC 2463 (ICMPv6 Specification), 2.4 e: 
"An ICMPv6 error message MUST NOT be sent as a result of receiving a packet destined to an IPv6 multicast address."
But two exceptions to this rule:
  Type 2: Packet too big (Path MTU Discovery for Multicast)
  Type 4: Parameter Problem, Code 2
Mitigation option:
Rate limit these two ICMPv6 message types
Notes: amplification  all multicast receivers send reply
The Smurf Attack is a way of generating significant computer network traffic on a victim network.

## Slide 77: What else?
Notes: Filter tunnels
Host side measures

## Slide 78: Filter Tunnels
Block unintended tunnel traffic (IPv4 Firewall)
  as discussed in detail in section "Securing Transition Mechanisms"
    IPv4: Protocol 41; UDP-Port 3544
    traffic to 192.88.99.1 (6to4 anycast server)
    …
Inspection of intended tunnel traffic
  If you allow tunnel traffic through the perimeter firewall usually it's not possible to define any granular policy 
  all IPv6 traffic is allowed then without any further control

## Slide 79: Additional security measures at Host (Server)
Enable / configure local paketfilter for IPv6
MS Windows
  supported since XP SP2, Server 2003 SP1
  in-/outbound & stateful since Vista and Server 2008
Linux (depending on Distri and Kernel)
  stateful since later versions of kernel 2.6 netfilter/ip6tables, ufw
BSD (OpenBSD, FreeBSD, NetBSD, OS X)
  pf, ipfw, ipfilter
3rd party Host based IPS (e.g. Cisco Security Agent)
Notes: for IP ranges, ICMPv6 types/codes, Stateful
DPI?
rate limiting?

## Slide 80: Conclusion
Understand IPv6 firewall issues prior to purchasing or deployment
Configure firewalls according to recommendations (ICMPv6, Extension Headers, Fragmentation, Multicast, Tunnels)
Start with a best effort approach…
…and review & improve along the way (availability of new features, emerging best practice)
Consider adding a layer of Server / Host security to your security concept

## Slide 81: Reconnaissance (a.k.a. Network Scanning)

## Slide 82: Reasons to scan a network?
Identify hosts on the network for
Penetration Testing
Defensive Security Scanning
Attacking!
But what's the difference to IPv4?
Notes: PT: mandate sbdy to test your network from outside for weaknesses (temporary, report, repeat after 1 year)
DSS: ongoing approach to scan network for weaknesses
Reconnaissance is always the first step.

## Slide 83: It's not possible anymore…
Sequentially scanning IPv6 net is not feasible anymore
/64 can have 1.8e^19 hosts
= 4'294'967'296 times the size of the IPv4 address space
This will take decades
t∞

## Slide 84: It's not still possible anymore…
You have to be smarter!
DNS bruteforcing on common hostnames
  using a dictionary
  or sequential a,aa,aaa,aab
Alive bruteforcing on typical addresses
  low range: ::1,::2,::3,…
  DHCP: sequential ranges 1000-2000 (find one, got all)
  Serviceport in IP addresses numbers: ::80,::53,53:1,53:2
  Autoconfiguration with MAC: 24 Bit are per Vendor-ID, 24 Bit must be guessed (16'777'216)
  Addresses using words 2001:db8::cafe:f00d:babe:beef
  other guessable patterns
Notes: Administrators like orderliness and structure  easy to guess for sbdy else

## Slide 85: Some research has been done by M. Heuse:
DNS bruteforcing: common hostnames
  with 1900 words get 90% of systems in DNS
Alive bruteforcing: typical addresses
  with 2000 addresses get 66% of the systems
Combined (and use of brain):
  ca. 90-95% of servers are found
Target Discovery is still possible

## Slide 86: Example: Finding hosts in DNS for target.org
use dnsdict6 with 'xlarge' built-in dictionary
dnsdict6 –x target.org
  apollo.target.org ==> 2001:beef:123:8:20c:29ff:fe3d:903
  ares.target.org ==> 2001:beef:123:8:20c:29ff:fea0:11fc
  argos.target.org ==> 2001:beef:123:8:20c:29ff:fea0:2121
  athena.target.org ==> 2001:beef:123:8:20c:29ff:fea0:2ffc
  […]
  Found 72 hosts and 60 unique ip-addresses for target.org
Notes: probes all entries of the dictionary against DNS

## Slide 87: Example: Finding live IPs of target.org
ping6 www.target.org (to get an idea of the used ip-pattern)
2001:beef:123:1::5
use alive26 with a known or guessed pattern
alive26 -d eth1 2001:beef:123:0-ff:0:0:0:0-1f
  Alive: 2001:beef:123:1::5 (www.target.org) [ICMP echo-reply]
  Alive: 2001:beef:123:2::4 (logon.target.org) [ICMP echo-reply]
  Alive: 2001:beef:123:3::1 (sales.target.org) [ICMP echo-reply]
  Alive: 2001:beef:123:a::9 (control.target.org) [ICMP echo-reply]
  […]
  Scanned 8192 addresses and found 138 systems alive
Notes: afterwards you can cont. with nmap like in v4

## Slide 88: More help from DNS / DNSSEC
Try DNS Zone Transfer to read complete zone file
dig @<nameserver> <domain> axfr
 seldom possible by now
DNSSEC Zone Walking (NSEC records are chained)
dnssecwalk <nameserver> <domain>
 corrective with NSEC3 (bind 9.6.0)
Notes: dnssecwalk merapi.switch.ch switch.ch

## Slide 89: If the attacker is already in the LAN
ping multicast addresses
  e.g.Link-local scope all nodes multicast address ff02::1
    ping6 –I eth1 ff02::1
    alive26 eth1 ff02::1
  doesn't work from Windows
  doesn't work for all targets
Sniffing
  e.g. listen to Neighbor Discovery Protocol
Neighbor Cache
  the equivalent to IPv4 ARP chache
    Linux: ip -6 neigh
    Windows: netsh interface ipv6 show neighbors
    Cisco: show ipv6 neighbors
Notes: afterwards you can cont. with nmap like in v4

## Slide 90: Target Discovery – Mitigation?
Use of static random addresses & unguessable DNS names? (hmm….)
Privacy extensions? (hmm….)
Any place where IPv6 addresses are listed will become more attractive for attackers (DNS, DHCP records, Logfiles…)  protect them
also mitigate Remote Neighbor Cache Exhaustion Attack
  A scan floods neighbor cache table (fast)
  Rate limiting, Ingress Filtering (see Section Perimeter)
Notes: 1. only if you really want to hide a server

## Slide 91: Finding IPv6 prefixes of an organization
RIPE DB provides full text search:
Target  IPv6 prefixes or ASN
  https://apps.db.ripe.net/search/full-text.html
Hurricane Electric provides prefix search for ASNs
ASN  Prefixes
  http://bgp.he.net/ASnnnn#_prefixes6
Notes: afterwards you can cont. with nmap like in v4

## Slide 92: Reconnaissance
dnsdict6 –x target.org
alive26 -d eth1 2001:beef:123:0-ff:0:0:0:0-1f
dnssecwalk merapi.switch.ch target.org
  https://apps.db.ripe.net/search/full-text.html
  http://bgp.he.net/ASnnnn#_prefixes6
Exercise
Use RIPE, HE, dnsdict, alive26, dnssecwalk to discover hosts of a target.

## Slide 93: More Info on IPv6 reconnaissance
D1T2 - Marc Heuse - IPv6 Insecurity Revolutions.pdf
http://conference.hitb.org/hitbsecconf2012kul/materials/
Hogg/Vyncke "IPv6 Security", Chapter 2
Search internet for "Remote Neighbor Cache Exhaustion Attack", "IPv6 Destination Guard"
Notes: verschiedene Absenderadressen
Privacy Extensions: wechselnde Adressen
PE nicht immer abschaltbar (Mobile OS)
Nachvollziehbarkeit?!
Logs / Tracing
Abhilfe
802.1.x Authentifizierung in Netzwerken
DHCPv6

## Slide 94: NAT and Security

## Slide 95: NAT
Quote from RFC 2993 – "Architectural Implications of NAT":
"The arguments pro & con frequently take on religious tones, with each side passionate about its position."
NAT is great for Topology Hiding!!
NAT destroys End-to-End-Principle!
NAT isn't about security!

## Slide 96: Let's look into the NAT RFC 1631 (May 1994)
4. Conclusions
NAT may be a good short term solution to the address depletion and scaling problems. This is because it requires very few changes and can be installed incrementally.
NAT has several negative characteristics that make it inappropriate as a long term solution, and may make it inappropriate even as a short term solution.
Notes: May 1994

## Slide 97: NAT (NAPT, PAT)
NAT technically consists of two things:
Address Translation
  rewriting parts of the headers
Stateful Inspection
  stateful correlation of inbound packets to existing outbound flows

## Slide 98: Security provided by NAT
Address Translation hides internal hosts and topology (to a certain level)
Fingerprinting gets more difficult
(depends on the complexity of the NAT)
Stateful Inspection prevents inbound Internet connections
Stateful filtering doesn't require NAT!
SI can/should be done by the Firewall
Notes:   (see RFC 5902, section 2.4.3 on NAT complexity details)
Other Non-security features: NAT avoids internal renumbering (but Unique Local Addresses)

## Slide 99: The essence of "NAT security"
Increased NAT complexity
=
increased obfuscation of internal network
+
decreased reachability
  (see RFC 5902, section 2.4.3 on NAT complexity details:
  Use of one-to-many NAPT mappings, randomness over time of the mappings, short mapping lifetimes, use of re-writing in IP header fields such as TTL)
Notes:   (see RFC 5902, section 2.4.3 on NAT complexity details)
Tradeoff

## Slide 100: Food for thought
Beware of the “It’s how we’ve always done it” trap
  NAT has always been a workaround!
Re-think the benefit & cost of NAT in your environment...
  operational cost / network management
  application level problems
  broken end-to-end security
...and consider using the money for "real" security
Anticipate future network requirements
  It's difficult to add end-to-end-capabilities later

## Slide 101: NAT related IPv6 concepts

## Slide 102: ULA – Private address space in IPv6
ULA "Unique local addresses"
private address space for IPv6
FD (1111 1101)+40 Bit random  /48 for internal use
can be used locally, will be filtered on network edge
random number should prevent any possible conflicts between organizations that merge or collaborate

## Slide 103: Network Prefix Translation (NAT66)
NPT "IPv6-to-IPv6 Network Prefix Translation" RFC 6296
  possible solution for address independency
  and multihoming (without BGP)
  1:1 address translation (not 1:many)
  it's stateless
  modifies the IPv6 header
  breakes IPsec
ULA address space: fd20:010d:08b5::/48
ISP prefix: 2001:db8:beef::/48
(Optional Second ISP prefix: 2001:db8:cafe::/48)
For an internal host with the address fd20:010d:08b5:babe::8:beef external presentation of that host to provider 1 would be 2001:db8:beef:babe::8:beef (and optional to provider 2 would be 2001:db8:cafe:babe::8:beef).

## Slide 104: NAT64/DNS64
Used in IPv6-only networks
Enables IPv6-only clients to access IPv4-only Server
Based on DNS response modifications
If no AAAA exists for an address resolution, the DNS64 enabled resolver returns an AAAA response with a prefix of a NAT64 router plus embedded IPv4 address:
    Prefix: 64:ff9b::/96
    Address: 64:ff9b::c000:0201
    Or 64:ff9b::192.0.2.1
The client then initiates an IPv6 connection to this IPv6 address
the NAT64 router does IPv6 to IPv4 translation
  Stateful
See RFC6146 / RFC6147

## Slide 105: Recommended Reading
RFC 4864 "Local Network Protection for IPv6"
  How perceived benefits of NAT can be provided with local network protection measures
RFC 5902 "IAB Thoughts on IPv6 Network Address Translation"
  (IAB = Internet Architecture Board)
NAT66 Discussion Archive
  https://www.ietf.org/mailman/listinfo/nat66

## Slide 106: Final notes

## Slide 107: Bottom line: How IPv6 affects IT-Security
Higher complexity (protocol and network)
Lower maturity (especially security devices)
Less Know-how / experience
New / more Attack vectors
Less visibility (Monitoring)
Multiprotocol Correlation issues
IPv6 risks also in "IPv4-only" network (Autoconfiguration, Tunnels)
Notes: Questions so far?

## Slide 108: Questions to ask yourself
Do you monitor IPv6 traffic on your network?
Do your firewalls filter (tunneled) IPv6 traffic?
Are all your tools Dual-Protocol-ready?
Do you have enough know-how about IPv6 and its specific attacks to detect them?
If you rely on IP-based Access Control, do you maintain it for both protocols?
Can you correlate multi protocol attacks?
Do you have IPv6 requirements for new / ongoing projects and procurement
Notes: Best remedy:
 Deploy IPv6 and enforce IPv6 security policies

## Slide 109: Recommended IPv6 Security Assessment Tools
Tool suite | Description | Platform / License
THC The Hacker Choice IPv6 Attack Toolkit Marc Heuse & others | lots of small tools (≈70) poorly documented pioneer work C library available | C Linux GNU/AGPL
SI6 Networks Security assessment and troubleshooting toolkit for IPv6 Fernando Gont | a few comprehensive tools (≈12) lots of parameters well documented mature | C Linux/xBSD/OS X GNU/GPL
chiron All-in-one IPv6 Penetration Testing Framework Antonios Atlasis | Craft arbitrary IPv6 packets to test IDS/IPS evasion And other interesting tools | Python/Scapy (modified) Linux GNU/GPL
Notes: likely also other tools around / arrive soon
Criteria:
Coverage – How many tools / test cases
Maturity – beta version or well tested
Development – Does somebody care?
Extensibility – Can you add your code / test cases?
Documentation – Is there a current / extensive documentation available

## Slide 110: Example Setup with 5 VMs (Attacker, 2 Victims, Router, Webserver)
R1
SW1
SW2
Attacker
Using THC IPv6 attack toolkit
Win7
08:00:27:AA:AA:AA
fe80:a00:27ff:feaa:aaaa
2001:db8:1::a00:27ff:feaa:aaaa
GW: fe80::a00:27ff:fe11:1111
08:00:27:BB:BB:BB
fe80:a00:27ff:febb:bbbb
2001:db8:1::a00:27ff:febb:bbbb
GW: fe80::a00:27ff:fe11:1111
Randomize Identifiers disabled
08:00:27:66:66:66
fe80:a00:27ff:fe66:6666
2001:db8:1::a00:27ff:fe66:6666
GW: fe80::a00:27ff:fe11:1111
Privacy Extensions disabled
2001:db8:2::2
GW: 2001:db8:2::1
eth0: forwarding enabled
2001:db8:1::1
fe80::a00:27ff:fe11:1111
radvd:
Prefix 2001:db8:1::/64
eth1:
2001:db8:2::1
﻿Webserver:
http://[2001:db8:2::2]/
Notes: EUI-64 insert FFEE to get 64 Bits (from 48 Bit MAC)
Modified EUI-64: toggle Bit 7 (08=>0A)
0000 i000  8
0000 i0i0 =>10=>A
Show 3 clients live

## Slide 111: Get & Install THC IPv6 Attack tools
Download thc-ipv6-[Version].tar.gz from thc.org
Required: Linux 2.6 or higher
Install
  sudo apt-get install libssl-dev libpcap-dev
  tar -xzf thc-ipv6-n.n.tar.gz
  cd thc-ipv6-n.n/
  make
  sudo make install
  make clean

## Slide 112: Get & Install SI6 IPv6 Attack tools
Download from github.com/fgont/ipv6-toolkit
Tested on: Debian GNU/Linux 6.0, FreeBSD 9.0, NetBSD 5.1, OpenBSD 5.0, Ubuntu 11.10, Mac 0S 10.8.0
Install
  sudo apt-get install libpcap-dev
  unzip ipv6-toolkit-master.zip
  cd ipv6-toolkit-master/
  sudo make all
  sudo make install
  make clean

## Slide 113: Recommended Resources
S. Hogg/E.Vyncke: Cisco Press “IPv6-Security"
NIST - Guidelines for the Secure Deployment of IPv6
Mailing List ipv6hackers run by SI6
IPv6 Security Whitepaper, Slides and Videos from Eric Vynce, Fernando Gont, Marc Heuse, Scott Hogg, Enno Rey, Antonios Atlasis
https://www.internetsociety.org/deploy360/ipv6/security/
Notes: NIST = US National Institute of Standards and Technology

## Slide 114: Requirements for (Security) Network Equipment - Some Resources
RIPE: RIPE-554 "Requirements for IPv6 in ICT Equipment"
  RIPE document that lists mandatory / optional RFCs for different types of equipment
  Contains a proposed text for tenders / RFPs
  http://www.ripe.net/ripe/docs/current-ripe-documents/ripe-554
IPv6-Forum: IPv6 Ready Logo Program
  Certification Program that covers basic IPv6 requirements and some advanced features, but it is not exhaustive.
  http://www.ipv6ready.org/
NIST/USGv6: IPv6 Profile and Testing Program
  http://www.antd.nist.gov/usgv6/
Notes: The IPv6 Forum is a world-wide consortium of Internet vendors, Industry Subject Matter Experts, Research & Education Networks, with a clear mission to advocate IPv6.
National Institute of Standards and Technology: US Government IPv6
Others:
DOD IPv6,
EU-Project GEN6 http://www.gen6.eu/home
Forschungsprojekt „IPv6-Profile“ für die öffentliche Verwaltung (Fraunhofer FOKUS): http://www.fokus.fraunhofer.de/de/elan/projekte/national/ipv6/index.html

## Slide 115: IPv6 Excuse Bingo
https://ipv6bingo.com/

## Slide 116: CVE entries containing IPv6
https://nvd.nist.gov/vuln/search/results?form_type=Basic&results_type=overview&query=IPv6&search_type=all

## Slide 117: 5 recommendations for a secure IPv6 strategy

## Slide 118: 1. Secure existing Operations
Do you have a IPv6 Latent Threat risk in your network?
If yes take steps against it:
  Deactivate IPv6 or SLAAC where reasonable
  Filter tunnel traffic at the perimeter
  Update your monitoring (Rogue Router Advrts.)
Notes: immer dann, wenn aktuelle Betriebssysteme vorhanden sind und IPv6 nicht berücksichtigt wurde
    Tunneltraffic filtern: IPv4 Protocol-Type 41, IPv4 UDP-Port 3544

## Slide 119: 2. Raise awareness at Management level
Has IPv6 arrived on the IT Management Agenda?
    Priority– Ressources – Budget
Do you have an IPv6 Integration Strategy?
    leverage existing life-cycles and projects
    realistic, phased roadmap
    Define a IPv6 Transition Manager
Make sure IT-Security is involved!
    e.g. Security-Devices, Design decisions, NAT, Adressing plan, Security-Policy update
Notes: no patchwork and downstream Security

## Slide 120: 3. Build up Know-how
Define a Training Plan
    different people (roles) need different knowledge
Build up a Testing Lab
  to gain experiences & to test equipment
Perform a Pilot project
    not critical but also not only in the lab
Inform and learn from others
  network-wg, security-wg, Swiss IPv6 Council,…
Notes: Build a test lab that replicates your entire network if you can afford to
Understand IPv6 before you deploy it!

## Slide 121: 4. Take into account the IPv6 readiness of your Security equipment
  Have an Inventory of your security equipment
  Define your IPv6 Requirements
  Do Vendor Management (IPv6-Roadmap?)
  Update Purchasing Guidelines
  Define a Testplan
  Synchronise deployment with security readiness!
Notes:   Ressources: RIPE-554, NIST USGv6, IPv6 Ready Logo

## Slide 122: 5. Recognize and use opportunities
  Start early – avoid time pressure
  Leverage existing Life cycles of equipment
  Add IPv6 to the requirements of existing projects
  Prefer step-by-step approach (know dependencies)
  If indicated: use opportunity for a network re-design
  Improve not degrade IT-Security by means of collaboration
Notes: z.B. Client-facing Services heute (DMZ), internes Netz nach 2015

## Slide 123
Thank you for your attention!
Contact the Author
frank.herberg@switch.ch
@frankherberg